## Slide 1: Eye Blinking Prediction using electroencephalography(EEG)
Yao Zou & Zuchen Zhang

## Slide 2: Introduction – motivation
application
Autonomous driving --- monitoring driver’s fatigue to improve driving safety
Medical assistance --- the important way for impaired person to communicate with the world
Prediction method
EEG signal prediction
Based on computer vision and image pattern recognize，but image is easily-effected by illumination, image scale, glasses
Nassr Alsaeedi* and Dieter Wloka “Real-Time Eyeblink Detector and Eye State Classifier for Virtual Reality (VR) Headsets (Head-Mounted Displays, HMDs)” Sensors (Basel). 2019 Mar; 19(5): 1121.
Królak, A. & Strumiłło, P. Univ Access Inf Soc (2012) 11: 409. https://doi.org/10.1007/s10209-011-0256-6
https://www.myvmc.com/investigations/electroencephalogram-eeg/
https://blog.safetyglassesusa.com/fighting-driver-fatigue/

## Slide 3: Introduction– Data
S. Vachiravel, Eye State Prediction using EEG Signal and C4.5 Decision tree algorithm, March 2016.
The objective of our project is to train an optimal model for eye blinking prediction based on 14-dimensional EEG signal. There are only 2 states of eye blinking which are open and closed, so basically we should construct a binary classifier to predict eye blinking.
Training data set consists of 10000 14-dimential observations with labels, 10-fold and leaving out first 10% cross validation methods will be implemented on it. Besides, testing data set with 4980 observations (unlabeled) is provided by Kaggle.
schematic of data collection

## Slide 4: Method – Feature Selective(FS)
Our training data are 14-dimensional, but to determine whether all dimensions are useful, we implement a feature selective method to generate new sequences of data from training data, and algorithm is shown as follows:
14 dim original measurement
.
.
.
The
sequence
of
new
feature
Sliding windows
Figure A: diagram of feature selective

## Slide 5: Method – FS with single decision tree
After feature Selective algorithm generates new training data set, each data set will be implemented with a single decision tree, by using the max vote principle we can get the final prediction result
Figure A: framework of ensemble learning with feature selective

## Slide 6: Experiments- single decision tree
Using 10-fold cross-validation on the training data, average error rate is the metric
For the same number of split nodes in the decision tree, single decision tree will perform better integrated with feature selective algorithm, which means a smaller average error
Besides, as the nodes becomes bigger, the average error rate will converge to a constant, which means there will be a limit of prediction ability for the model
Figure A: single decision tree vs FS-single decision tree

## Slide 7: Experiments-Adaboost implementation
We used the first 10% of the entire data as testing data and used the rest as training data.
We did not specify when to stop splitting decision tree of every level.
We want to optimize a hyperparameter, number of levels, of Adaboost. The optimization process is shown as follows.
Figure A. Error of Adaboost with the number of its levels increasing
It is demonstrated that when the number of levels is larger than 1000, the error rate of Adaboost on testing data converges to about 3.5%.

## Slide 8: Experiments-Adaboost & FS
In this experiment, we devise the Adaboost algorithm with max 500 split nodes for each tree, the max level is 300, based on previous experiment
Figure A. Adaboost vs FS integrated with Adaboost in different number of level
When level is less then 5, FS algorithm can help to augment prediction ability, but when level gets bigger, FS will be useless.

## Slide 9: Experiments-SVM(rbf kernel)
Using SVM classifier and optimizing the hype-parameter. The min error rate can be 2.716%
All the hype-parameters will be used to generate series of SVM
figure A: min objective optimization
figure B: hype-parameter optimization
figure C: best hyper-paramters

## Slide 10: Test in Kaggle
We fully train the model on the entire training data set with SVM, FS-SVM single decision tree, FS-single decision tree, Adaboost. Predict the testing data and evaluate the prediction on Kaggle
model | SVM(rbf) | FS&SVM(rbf) | Single tree( 500 splits) | FS & Single tree(500 splits) | Adaboost(500 levels)
Score(accuracy) | 0.97405 | 0.89061 | 0.80899 | 0.83138 | 0.95706
https://www.kaggle.com/c/compomicssummer2018/submissions

## Slide 11: Conclusion
By predicting the testing data set, we can conclude this new feature selective method can help to improve the performance of some weak classifiers, such as the single decision tree.
In this eye blink prediction task, SVM performs best among all the models, as well as Adaboost is another good prediction classifier.

## Slide 12: Reference
Nassr Alsaeedi* and Dieter Wloka “Real-Time Eyeblink Detector and Eye State Classifier for Virtual Reality (VR) Headsets (Head-Mounted Displays, HMDs)” Sensors (Basel). 2019 Mar; 19(5): 1121.
Królak, A. & Strumiłło, P. Univ Access Inf Soc (2012) 11: 409. https://doi.org/10.1007/s10209-011-0256-6
Noman, Md, et al. "Mobile-based Eye-Blink Detection Performance Analysis on Android Platform." Frontiers in ICT 5 (2018): 4.
Rihana, S., P. Damien, and T. Moujaess. "EEG-Eye blink detection system for brain computer interface." Converging Clinical and Engineering Research on Neurorehabilitation. Springer, Berlin, Heidelberg, 2013. 603-608.
S. Vachiravel, Eye State Prediction using EEG Signal and C4.5 Decision tree algorithm, March 2016.
Al-Taei, Ali. "Ensemble Classifier for Eye State Classification using EEG Signals." arXiv preprint arXiv:1709.08590 (2017).
Jain, Neha, et al. "Eye state prediction using EEG by supervised learning." International Journal of Science, Engineering and Technology 10 (2015).